## Wheel Loader 955T

Features
1. The wheel loader 955T is installed with Weichai engine.
2. Two forward and one reverse power shift transmissions are installed .
3. Combined sealing cylinder brings good sealing performance and reliability.

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length (with bucket on ground) | 7900(mm) |
| 2 | Width (to outside of wheels) | 2800(mm) |
| 3 | Bucket width | 2946(mm) |
| 4 | Height (to the top of the cab) | 3500(mm) |
| 5 | Wheel base | 3100(mm) |
| 6 | Tread | 2200(mm) |
| 7 | Min. ground clearance | 450(mm) |
| Main Technical Specification of Wheel Loader |
| 1 | Rated loading capacity | 5000(kg) |
| 2 | Operating weight | 16300(1±5%)kg |
| 3 | Rated bucket capacity | 3.0(m3) |
| 4 | Max. breakout force | 160KN |
| 5 | Max. dumping clearance | 3091(mm) |
| 6 | Dumping reach | 1090(mm) |
| 7 | Dumping angle at any position | ≥45° |
| 8 | Digging depth (with bucket bottom horizontal) | 165(mm) |
| 9 | Min. turning radius |
|  | (1) Outside of bucket | 6575(mm) |
|  | (2) Outside of rear wheel | 5970(mm) |
| 10 | Max. steering angle | 38o |
| 11 | Oscillating angle of rear axle | ±13o |
| 12 | Lifting time of bucket | ≤6.2(sec.) |
| 13 | Lowering time of bucket | ≤3.8(sec.) |
| 14 | Dumping time | ≤1.8(sec.) |
| 15 | Traveling speed (2 forward and 1 reverse) |
|  | (1) 1st gear (forward/reverse) | 12.1/16.5(km/h) |
|  | (2) 2nd gear forward | 37.4(km/h) |
| Diesel Engine of Wheel Loader |
| 1 | Model | Chinese Engine WD10G220E23 |
| 2 | Type | Direct injection, naturally aspirated, water cooled |
| 3 | Rated power | 162(kW) |
| 4 | Cylinder diameter/stroke | 126/130(mm) |
| 5 | Displacement of cylinder | 9.726(L) |
| 6 | Model of starting motor | KB-24V |
| 7 | Power of starting motor | 7.5(kW) |
| 8 | Voltage of starting motor | 24(V) |
| 9 | Rated speed | 2000(r/min) |
| 10 | Max. torque | >900(N.m) |
| 11 | Starting type | Electrical starting |
| 12 | Min. specific fuel consumption | <220g/kW.h) |
| 13 | Engine specific oil consumption | 0.95-1.77(g/kW.h) |
| 14 | Net weight | 1000(kg) |
| Transmission System of Wheel Loader |
| I. Hydraulic Torque Converter |
| 1 | Model | ZL50B-012 |
| 2 | Type of torque converter | 4-element, single stage |
| 3 | Torque ratio | 4 |
| 4 | Cooling type | Pressure oil circulating |
| 5 | Type of gearbox | Power shift, constant-mesh spur gear |
| 6 | Gear shift | 2 forward and 1 reverse gears |
| II. Axle and Tire |
| 1 | Type of main reducer | Spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 4.625 |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Gear ratio of final reducer | 4.929 |
| 5 | Total gear ratio | 22.795 |
| 6 | Max. drawing force | 150kN |
| 7 | Size of tire | 23.5-25-16PR |
| Working Device Hydraulic System of Wheel Loader |
| 1 | Model of oil pump | JHP2080S |
| 2 | System pressure | 19MPa |
| 3 | Model of distribution valve | HDS-32II-YL19 |
| 4 | Dimension of lifting cylinder(D×L) | Ф160×90×705(mm) |
| 5 | Dimension of tilting cylinder(D×L) | Ф180×90×530(mm) |
| Steering System |
| 1 | Type | Middle articulated frame, full-hydraulic steering |
| 2 | Model of steering pump | JHP2080S |
| 3 | Model of redirector | TLF1-E1000B+FKB6020 |
| 4 | Model of priority valve | YXL-F250F-N7 |
| 5 | System pressure | 16MPa |
| 6 | Dimension of steering cylinder | Ф90×400(mm) |
| Braking System |
| 1 | Type of service brake | Caliper disc brake, air-over-oil activated 4 wheel brake |
| 2 | Air pressure | 6-7.5(kgf/cm2) |
| 3 | Type of parking brake | Hand brake, flexible shaft control drum brake |
| Oil Capacity of Wheel Loader |
| 1 | Fuel(diesel) | 250(L) |
| 2 | Engine lubricating oil | 20(L) |
| 3 | Oil for converter and gear box | 45(L) |
| 4 | Oil for hydraulic system | 180(L) |
| 5 | Oil for driving axles (F/R) | 26(L) |
| 6 | Oil for planetary reducer | 14(L) |
| 7 | Oil for braking system | 3(L) |