## CLTL70C Asphalt Paver

Features of Asphalt Paver
1. Rigid, durable crawler traveling track provides powerful traction. 
2. Scraper bars and material distributors are alternately mounted to either left or right side. 
3. Centralized lubrication system keeps hot and movable parts well lubricated. 
4. Self-leveling sensor ensures the paved mat is flat and up to standard. 
5. Fuel oil cleaning system cleans up dirty oil fast, thereby reducing workload. 
6. Extendable screed arm 
7. Driver’s cabin offers a broad view, with movable console.

Technical Specification

| Model | CLTL70C |
| --- | --- |
| Length×Width×Height(mm) | 6565×3210×3050 |
| Total weight(t) | 16-19.5 |
| Diesel engine type | WeiChai BF6L 913 |
| Rated output(KW) | 112 |
| Basic paving width(mm) | 3000 |
| Maximum paving width(mm) | 7000 |
| Maximum thickness of paving (mm) | 300 |
| Minimum thickness of paving (mm) | 20 |
| Traveling speed(Km/h) | 0.9-2.86 |
| Paving speed(m/min) | 2-3.6 |
| Hopper capacity(t) | 12 |