## Wheel Loader 996

The wheel loader is equipped with a reliable original Cummins engine, ZF transmission case and torque converter. Also, it comes with original ZF wet-type axles with multi-disc limited-slip differentials. Its KD switch assures higher efficiency and easy operation. Its 24° cone-shaped seal cylinder comes with high sealing performance.

In addition, the wheel loader comes with a single brake valve, dual pipe fully hydraulic brakes and central lubrication system.

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length(with bucket on ground) | 9415(mm) |
| 2 | Width(to outside of wheels) | 3438(mm) |
| 3 | Bucket width | 3500(mm) |
| 4 | Height(To the top of the cab) | 3780(mm) |
| 5 | Wheel base | 3645(mm) |
| 6 | Tread | 2450(mm) |
| 7 | Min. ground clearance | 461(mm) |
| Main Technical Specification |
| 1 | Rated load | 9000(Kg) |
| 2 | Operating weight | 31620kg |
| 3 | Rated bucket capacity | 5.1(m3) |
| 4 | Max. breakout force | 202KN |
| 5 | Max. Drawing force | 261 KN |
| 6 | Max. dump clearance | 3300(mm) |
| 7 | Dump reach | 1410(mm) |
| 8 | Dump angle at any position | ≥45° |
| 9 | Digging depth | 250(mm) |
| 10 | Min. turning radius |
|  | (1)Outside of bucket | 7511(mm) |
|  | (2)Outside of rear wheel | 6614(mm) |
| 11 | Pivot angle frame | 40° |
| 12 | Oscillating angle of rear axle | +12o |
| 13 | Lifting time of bucket | 6.0(sec.) |
| 14 | Lowering time of bucket | 3.4(sec.) |
| 15 | Dumping time of bucket | 1.6(sec.) |
| 16 | Traveling speed(Km/h) |
|  | (1)1st gear (Forward & reverse) | 6.4 |
|  | (2)2nd gear (Forward & reverse) | 11.94 |
|  | (3)3rd gear (Forward & reverse) | 18.72/25.92 |
|  | (4)4th gear (Forward) | 37 |
| Diesel engine |
| 1 | Model | Original Cummins M11-C335 M11-C335 |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 250(Kw) |
| 4 | Inter-bore of cylinder/stroke | 125/147(mm) |
| 5 | Total exhaust of cylinder | 10.8(L) |
| 6 | Model of starting motor | 39MT-HD |
| 7 | Power of starting motor | 8(KW) |
| 8 | Voltage of starting motor | 24(V) |
| 9 | Rated speed | 2100(r/min.) |
| 10 | Max. Torque | 1674(N.m) |
| 11 | Starting type | Electric |
| 12 | Min. specific fuel consumption | 215(g/Kw.h) |
| 13 | Engine specific oil consumption | 1.0 (g/Kw.h) |
| 14 | Net weight | 984(Kg) |
| Transmission System |
| 1. Torque Converter |
| 1 | Type | 3-element.single stage |
| 2 | Torque ratio | 2.511 |
| 3 | Max. Dia. of flow path | 400(mm) |
| 4 | Cooling type | Pressure oil circulating |
| 2. Gear Box |
| 1 | Model | ZF4WG310 |
| 2 | Type | Power shift, spur gear constant-mesh |
| 3 | Gear shift position | 4 Forward and 3 reverse gears |
| 3. Axle and Tire |
| 1 | Type of main reducer | Spiral gear single stage |
| 2 | Gear ratio of main reducer | 5 |
| 3 | Type of final reducer | single stage planetary |
| 4 | Gear of ratio of final reducer | 5.4 |
| 5 | Total ratios | 27 |
| 6 | Size of tyre | 29.5-25 -22PR(L-3) |
| Working Device Hydraulic System |
| 1 | Model of oil pump | AV0V0 100 DRS/53R-VWC12G60 |
| 2 | System pressure | 26(MPa) |
| 3 | Model of Muti-way directional valve | M6-1416-00/3M6-22EH |
| 4 | (d*l)Dimension of lifting cylinder | 2-Ф200*110*790(mm) |
| 5 | (D*l)Dimension of tilting cylinder | 1-Ф225*125*575(mm) |
| Steering System |
| 1 | Type | Middle articulated frame. full hydraulic power |
| 2 | Model of steering pump | HA10VO110DFR1/31R-VWC 12 H00 |
| 3 | Model of redirector | 150-7170 |
| 4 | Model of Magnify valve | 150F0040 |
| 5 | System pressure | 21MPa |
| 6 | Dimension of steering cylinder | 2-Ф110*55*486(mm) |
| Brake System |
| 1 | Type of traveling brake | Wet type multi-disc brakeSingle brake valve& dual pipe, full hydraulic brake |
| 2 | Braking pump | AZPF-11-016-RRR20KB-S0023 |
| 3 | System pressure | 16 (MPa) |
| 4 | Type of emergency brake | Lower pressure alarm brake |
| 5 | Type of parking brake | Electric control brake |
| Oil Capacity |
| 1 | Fuel(diesel) | 480(L) |
| 2 | Engine oil | 32(L) |
| 3 | Oil for converter and gear box | 43(L) |
| 4 | Oil for hydraulic system | 260(L) |
| 5 | Oil for driving axles(F/R) | 51(L) for each |