## Motor Grader 719H

Features of Motor Grader-719H:
1. Equipped with reliable ShangChai SC11CB195G2B1 engine or genuine Cummins engine
2. Sing-handle electro-hydraulic controlled power-shift T/M, 6 forward & 3 reverse shifts makes operation easy and convenient
3. Hydraulic lock, auto lock/unlock NO-SPIN differential ensures stability and powerful traction
4. Ideal axel load allocation provides excellent stability while cutting hard surface
5. Serviceable, efficient hydraulic system enables every part to be fully used
6. Box-typed frame and advanced T/M enable it to complete heavy-duty work
7. A wide working range is accomplished through flexible blade suspension system and articulated frame

Specifications of Motor Grader-719H:

| Overall Dimension |
| --- |
| 1 | Length | 9385mm | 9235mm |  |
| 2 | Width | 4268mm |  |
| 3 | Height(To the top of the cab) | 3370mm |  |
| 4 | Wheel base | 6150mm | 6100mm |  |
| 5 | Tread | 2120(mm) |  |
| Main Technical Specification |
| 1 | Operating weight | 15800kg | 15900kg |  |
| 2 | Blade length | 4268mm |  |
| 3 | Blade height | 645mm |  |
| 4 | Shovel Blade thickness | 18mm |  |
| 5 | Max lifting height | 450mm |  |
| 6 | Max grading depth | 535mm |  |
| 7 | Min. turning radius | 7400mm |  |
| 8 | Pivot angle frame | ±26° |  |
| 9 | Max turning angle(front wheel) | +49° |  |
| 10 | Oscillating angle of front axle | 32° |  |
| 11 | Front axle center ground clearance | 610mm |  |
| 12 | Traveling speed(Km/h),6 forward and 3 reverse |
|  | (1) Ⅰ gear forward | 6.5 |  |
|  | (2) Ⅱ gear forward | 11.4 |  |
|  | (3) Ⅲ gear forward | 14.6 |  |
|  | (4) Ⅳ gear forward | 24.8 |  |
|  | (5) Ⅴ gear forward | 30 |  |
|  | (6) Ⅵ gear forward | 49.2 |  |
|  | (7) Ⅰ gear reverse | 6.5 |  |
|  | (8) Ⅱ gear reverse | 14.6 |  |
|  | (9) Ⅲ gear reverse | 30 |  |
| Diesel engine |
| 1 | Model | Cummins engine 6CTAA8.3-C185 (TIER2) | ShangChai SC11CB195G2B1 Engine |  |
| 2 | Type | Direct injection. Turbocharged. | Direct injection. Turbocharged. Water cooling |  |
| 3 | Rated output | 138 kW | 143(1±5%)(kW) |  |
| 4 | Inter-bore of cylinder/Stroke | 114/135 (mm) | 121/152 (mm) |  |
| 5 | Total exhaust of cylinder | 8.3(L) | 10.48(L) |  |
| 6 | Power of start motor | 7.5(KW) | 7.5(KW) |  |
| 7 | Voltage of starting motor | 24(V) | 24(V) |  |
| 8 | Rated speed | 2200(r/min) | 2200(r/min.) |  |
| 9 | Max. Torque | 902(N.m) /(1400r/min) | 748±6%(N.m)/(1400r/min) |  |
| 10 | Starting type | Electric | Electric |  |
| 11 | Min. specific fuel consumption | 211(g/Kw.h) | 230(1±5%)(g/kw.h) |  |
| 12 | Net weight | 617(kg) | 960(kg) |  |
| Transmission System |
| 1.Torque Converter |
| 1 | Model | WG180 (ZF technology) |  |
| 2 | Type | 3-elements.single stage |  |
| 3 | Torque ratio | 2.35 |  |
| 4 | Cooling type | Pressure oil circulating |  |
| 2.Transmission case |
| 1 | Model | WG180 (ZF technology) |  |
| 2 | Type | power shift, single-shift lever, natural-shift lock device |  |
| 3 | Gear shift position | 6 Forward and 3 reverse gears |  |
| 3.Axle and Tire |  |
| 1 | Type of main reducer | spiral bevel gear, single stage |  |
| 2 | Gear ratio of main reducer | 3.583 |  |
| 3 | Type of final reducer | Single stage chain-drive |  |
| 4 | Gear of ratio of final reducer | 3.75 |  |
| 5 | Gear ratio | 13.436 |  |
| 6 | Tandem drive | Double row roller-chains |  |
| 7 | Size of tire | 17.5-25-12PR(standard) 13.00-24-12PR(optional) |  |
| Working Device Hydraulic System |  |
| 1 | Model of oil pump(include steering pump) | CBGj2045/1025 |  |
| 2 | System pressure | 17.5MPa |  |
| 3 | Model of distribution valve | HUSCO5000-D |  |
| 4 | Hydraulic check valve | Italy MTC technology |  |
| 5 | Model of oil motor | EATON, JS-130 |  |
| Steering System |
| 1 | Type | Fore Tire deflexion |  |
| 2 | Model of steering gear | BZZ1-E160B/ FKA-163022 |  |
| 3 | System pressure | 16MPa |  |
| Brake System |
| 1 | Type of traveling brake | Hydraulic assisted and inner-expanding brake |  |
| 2 | System pressure | 10MPa |  |
| 3 | Type of parking brake | Mechanical and inner-expanding brake |  |
| Cylinder size |  |
| 1 | front wheel steering cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 2－Ф50*35*320(mm) |  |
| 2 | Front wheel leaning cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 1－Ф80*40*160(mm) |  |
| 3 | Blade lifting cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 2－Ф80*50*1045(mm) |  |
| 4 | Power tilting cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 1－Ф80*40*300(mm) |  |
| 5 | Hinge turning cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 2－Ф90*50*370(mm) |  |
| 6 | Drawbar shift cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 1－Ф80*45*450(mm) |  |
| 7 | Blade side shift cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 2－Ф80*50*1250(mm) |  |
| 8 | Scarifier cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 1－Ф90*50*300(mm) |  |
| 9 | Front blade cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 1－Ф90*45*400(mm) |  |
| 10 | Ripper cylinder | Type | Double acting piston |  |
|  |  | No-bore X rod X stroke | 1－Ф100*50*635(mm) |  |
| Oil Capacity |
| 1 | Fuel(diesel) | 300L | 340L |  |
| 2 | Engine lubricating oil | 24L | 27L |  |
| 3 | Oil for converter and gear box | 28L |  |
| 4 | Oil for hydraulic system | 80L | 90L |  |
| 5 | Oil for driving rear axles | 18L |  |
| 6 | Tandem box | 90L |  |

Sound quality construction machinery and construction equipment including wheel loaders, road rollers, motor graders, backhoe loaders, skid steer loaders, pavers, concrete truck mixers, Truck Mounted Crane and other high quality construction machinery, construction equipment and engineering vehicle exist in Changlin.