## Backhoe Loader 630

Features of Backhoe Loader 630:
1. Equipped with reliable genuine Cummins engine
2. 4 forward & 4 reverse synchromesh mechanical shift transmission
3. Combined seal cylinder obtains high seal performance and more reliability
4. Improved loader and backhoe performance
5. CARRARO wet type rear axle with multi-disc brake& CARRARO front axle
6. New-type cab with more space, increases comfort and visibility
7. With 2 wheel driving or 4 wheel driving for option

Specifications of Backhoe Loader 630:

| Overall Dimension |
| --- |
| 1 | Length(with bucket on ground) | 7085(mm) |
| 2 | Width | 2313(mm) |
| 3 | Load Bucket width | 2313(mm) |
| 4 | Height(To the top of the cab) | 2710 (mm) |
| 5 | Height(To the top of the digging pole) | 3424 (mm) |
| 6 | Wheelbase | 2155.5(mm) |
| 7 | Back wheel Tread | 1700(mm) |
| 8 | Fore wheel Tread | 1880(mm) |
| 9 | Min. ground clearance | 355(mm) for 2WD 275(mm) for 4WD |
| Main Loading Technical Specification |
| 1 | Rated load | 1700(Kg) |
| 2 | Operating weight | 7600KG |
| 3 | Max lifting capability | >2500KG |
| 4 | Rated load bucket capacity | 1.0(m3) |
| 5 | Max. load breakout force | >60kN |
| 6 | Max. dump clearance | 2714(mm) |
| 7 | Max. Dump reach | 845(mm) |
| 8 | Dump angle at any position | ≥43.5° |
| 9 | Min. turning radius |
|  | (1) Outside of bucket | 5280(mm) for 2WD 5670(mm) for 4WD |
|  | (2) Center of front wheel | 3795 (mm) for 2WD 4380(mm) for 4WD |
| 10 | Lifting time of loading bucket | ≤4.5(sec.) |
| 11 | Lowering time of loading bucket | ≤3.5(sec.) |
| 12 | Dumping time | ≤1.5(sec.) |
| 13 | Traveling speed(Km/h),4 forward and 4 reverse |
|  | (1) Ⅰ gear forward | 6 |
|  | (2) Ⅱ gear forward | 9.6 |
|  | (3) Ⅲ gear forward | 20.5 |
|  | (4) Ⅳ gear forward | 38 |
|  | (1) Ⅰ gear reverse | 6.0 |
|  | (2) Ⅱ gear reverse | 9.6 |
|  | (3) Ⅲ gear reverse | 20.5 |
|  | (4) Ⅳ gear reverse | 38 |
| Main Digging Technical Specification |
| 1 | Rated digging bucket capacity | 0.3(m3) |
| 2 | Max. digging depth | 4405(mm) |
| 3 | Max. digging force | >50±10%kN |
| 4 | Max. digging radius | 5481(mm) |
| 5 | Max. dumping height | 3737(mm) |
| Diesel engine |
| 1 | Model | Cummins B4.5 | DongFeng 4BTA3.9-C110 |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated power / Rated speed | 74 (kW) / 2200(r/min) | 82 (kW) / 2200(r/min) |
| 4 | Displacement | 4.5(L) | 3.9(L) |
| 5 | Inter-bore of cylinder/stroke | 102/138(mm) | 102/120(mm) |
| 6 | Model, Voltage and Power of starting motor | ST9371 12(V) 4.8(kW) | ST 9501 12(V) 6(kw) |
| 7 | Model, Voltage and Starting Current of Alternator | EE9242 12(V) 95Amp | EE 9235 14(V) 70Amp |
| 8 | Max. Torque | 414(N.M) @1500RPM | 460N.m@1500RPM |
| 9 | Starting type | Electric |
| 10 | Min. specific fuel consumption | 207(g/Kw.h) |  |
| Transmission System |
| 1. Torque Converter |
| 1 | Model | CARRARO |
| 2 | Cooling type | Pressure oil circulating |
| 2. Transmission case |
| 1 | Model | CARRARO |
| 2 | Type | Synchromesh mechanical shift |
| 3 | Gear shift position | 4 Forward and 4 reverse gears |
| 3. Axle and Tire |
| 1 | Model | CARRARO |
| 2 | Type of main reducer | spiral bevel gear, single stage |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Max. steering angle | 55° |
| 5 | Tire type | 4WD fore tire12-16.5NHS-10PR |
| 2WD fore tire11L-16F3-12PR |
| Rear tire 19.5L-24R4-12PR |
| Working Device Hydraulic System |
| 1 | Model of oil pump | K2215(CASAPPA) |
| 2 | System pressure | 230(kgf/cm2) |
| 3 | Model of priority valve | WALVOIL SDS180 |
| Steering System |
| 1 | Type | Fore wheel Steering |
| 2 | Model of steering pump | K2215(CASAPPA) |
| 3 | Model of steering gear | 150-1219(DAIVFOSS) |
| 4 | System pressure | 140(kgf/cm2) |
| Oil Capacity |
| 1 | Fuel(diesel) | 151(L) |
| 2 | Engine lubricating oil | 11(L) |
| 3 | Oil for converter and gear box | 18.5(L) |
| 4 | Oil for hydraulic system | 110(L) |
| 5 | Oil for driving axles(F/R) | 7.6+17(L) |

Changlin always provide global customers with the best quality construction machinery products and construction equipment such as wheel loaders, motor graders, road rollers, pavers, concrete truck mixers and Truck Mounted Crane , etc.