## ZG3235-9/ZG3235-9C Excavator

Features
1. Our hydraulic excavator is equipped with a reliable original Cummins engine. 
2. It has a reliable hydraulic system that covers superior pumps, motor and valves. 
3. The hydraulic excavator comes with an electronic monitoring and control system that offers multifunctional LCD display function. 
4. With a stepped-up device, it suits use in mines. 
5. The hydraulic excavator is designed with strengthened X-shaped box structure.

Technical Parameters of ZG3235-9/ZG3235-9C Excavator

| Product model | ZG3235-9/ZG3235-9C |
| --- | --- |
| Length×Width×Height(mm) | 9840×2980×3160 |
| Operating weight(Kg) | 23000 |
| Rated bucket capacity(m3) | 1.1 |
| Max. digging depth(mm) | 6920 |
| Max. digging radius(mm) | 10180 |
| Max. digging height(mm) | 9562 |
| Max. digging force(KN) | 159 |
| Gradient capacity (%) | 70 |
| Diesel engine type | Cummins 6BTAA5.9-C178 |
| Rated output(KW) | 133 |