## CLQY130K-I Truck Crane

Truck crane CLQY130K-I is a full-terrain boom truck that integrates the flexibility of boom hoist with the mobility of truck. Superbly rugged 6-section boom features an oval cross section. Telescopic boom retracts and extends freely, and is powered by one single hydraulic cylinder. 3 extra long boom sections are powered separately by a hydraulic cylinder and available with self-elevating features for easy removal and set-up. A specialized 6-axle chassis comes with 12×6 drive and 12×8 power steering. Unique suspension system, typically found in a full-terrain crane, is used to allow a greater amount of wheel up and down movement (up to 100mm). Double leaf spring suspension uses two longitudinal leaf springs to ensure reliable transmission, reduce turning radius, and deliver excellent off-road performance. All these features contribute to a larger load bearing capacity. Maximum boom length: 58m, Maximum Height of Extra Boom: 86m.

Technical Specification

| Model | CLQY130K-I |
| --- | --- |
| Length×Width×Height(mm) | 14980×3000×3990 |
| Operating weight(Kg) | 54900 |
| Diesel engine type | Up VOLVO TAD720VE/ Down WeiChai WP13.480E30 |
| Rated output(KW) | 162/353 |
| Max load Moment(KN.m) | 4998 |
| Max. total rated lifting capacity (t) |  |
| Maximum gradeability(%) | 130 |
| Max. slewing speed(r/min) | 1.8 |
| Base boom length(m) | 13.1 |
| Maximum lifting range ability(m) | 59 |