## CLT100G-3 Bulldozer

Description
1. CLT100G-3 bulldozer is designed with a diesel engine by introducing advanced technologies from British Ricardo Company. As an energy-saving and eco-friendly product, it is made in compliance with national emission standards, providing low noise and high torque. 
2. Main clutch: The multi-disc dry clutch has the features of large torque reserve factor and reliable operation etc. 
3. Gearbox: 4F+2R mechanical gearshift transmission for easy operation, convenient maintenance and reliable use 
4. Steering clutch: The hydraulic power assisted steering clutch is a multi-disc dry clutch that can be easily maintained and operated. 
5. Transmission: Two-stage, straight-tooth and high-module gear transmission has the advantages of high reliability and strong load-bearing capacity etc. 
6. Adopting a luxurious cab and a rooftop air conditioning system for a comfortable operating environment 
7. The bulldozer can be optionally installed with various devices, such as straight-tilt blade, coal blade and angle blade, among others.

Specifications of CLT100G-3 Bulldozer

| Product model | CLT100G -3 |
| --- | --- |
| Length×Width×Height(mm) | 4190×2935×3020 |
| Operating weight(Kg) | 10400 |
| Diesel engine type | British Ricardo LR6A 3Z-23 |
| Rated output(KW) | 95 |
| Max. lift above ground(mm) | 830 |
| Max. drop below ground(mm) | 350 |
| Track width(mm) | 450 |