## CLTS80-3 Bulldozer

Description 
1. CLTS80-3 bulldozer is designed with a Dongfanghong LR4A3Z-22 supercharged engine for high power, low noise and low energy consumption. 
2. 4F+2R mechanical-gearshift countershaft transmission is applicable to a diverse range of operations. 
3. Rigid chassis and semi-rigid suspension are available. 
4. State-of-the-art control system and hydraulic power assisted steering system for flexible operation and less operator fatigue 
5. The driver’s cab is welded with profile steel for high strength, strong shock resistance and high safety. 
6. The bulldozer can be applied in narrow space, providing the advantages of flexible operation and high working efficiency. 
7. This product is configured with a heater. It can be optionally installed with an air-conditioner for cooling and heating purposes. 
8. Humanized design for convenient maintenance 
9. With high reliability and excellent power economy, this product is an ideal machine for engineering construction.

Technical Parameters of CLTS80-3 Bulldozer

| Product model | CLTS80-3 |
| --- | --- |
| Length×Width×Height(mm) | 4200×2934×2890 |
| Operating weight(Kg) | 9000 |
| Diesel engine type | British Ricardo LR4A 3Z-22 |
| Rated output(KW) | 70 |
| Max. lift above ground(mm) | 715 |
| Max. drop below ground(mm) | 357 |
| Track width(mm) | 600 |