## CLD230S Bulldozer

Characteristics 
CLD230S bulldozer is outfitted with NTAA855-C280S20 model Cummins engine, 3-element, single stage, single phase torque converter, 3F+3R power gearshift transmission, wet-type steering clutch and hydraulic bi-directional belt brake. Its working mechanisms include the servo controlled straight-tilt blade, traction device and hexagonal cab. This product can be optionally installed with an air-conditioning system.

Technical Parameters of CLD230S Bulldozer

| Product model | CLD230S |
| --- | --- |
| Length×Width×Height(mm) | 6060×4365×3460 |
| Operating weight(Kg) | 26920 |
| Diesel engine type | Cummins NTAA855-C280S20 |
| Rated output(KW) | 179 |
| Max. lift above ground(mm) | 1330 |
| Max. drop below ground(mm) | 550 |
| Track width(mm) | 1000 |