## CLT160-5 Bulldozer

Description
1. CLT160-5 bulldozer is equipped with a new generation of STEYR WD10G178E25 model supercharged diesel engine for high power, low oil consumption and high reliability. 
2. It adopts a wet clutch and a F5+R4 mechanical gearshift transmission for high efficiency. 
3. Hydraulically controlled steering and braking as well as pilot-operated blade and ripper for high flexibility, safety and reliability 
4. Adopting a three-stage air filter for extended engine lifespan and reduced operating costs 
5. The renowned brand instrument assembly is imported from a foreign country for high reliability and high-precision visual display. 
6. This machine can be optionally installed with numerous devices, such as straight-tilt blade and sanitation type blade etc.

Specifications of CLT160-5 Bulldozer

| Product model | CLT160-5 |
| --- | --- |
| Length×Width×Height(mm) | 5140×3390×3100 |
| Operating weight(Kg) | 17000 |
| Diesel engine type | WeiChai WD10G 178E25 |
| Rated output(KW) | 131 |
| Max. lift above ground(mm) | 955 |
| Max. drop below ground(mm) | 552 |
| Track width(mm) | 510 |